## Slide 1: Sequential Manipulation of Deformable Linear Object Networks with Endpoint Pose Measurements using Adaptive Model Predictive Control
Tyler Toner1,3, Vahidreza Molazedeh3, Miguel Saez3, Dawn M. Tilbury1,2, Kira Barton1,2
1 Department of Mechanical Engineering, University of Michigan
2 Robotics Department, University of Michigan
3 General Motors Research & Development

## Slide 2: Unstructured task automation
Industrial robots today: structured, repetitive tasks
Wire harness installation remains a manual operation
Unstructured Tasks
Task sequence cannot be fully predicted due to uncertainty (e.g., cable flexibility)
Manually programmed:
Fixed PLC logic and robot trajectories.
Goal
Enable unstructured robotic manipulation tasks.

## Slide 3: Wire harness installation
Main body wire harness, Ferrari 458 Italia
Wide variety of connector types
Figure: [Zhou et al. 2020]
Harness installation: Insert all terminals into their respective receptacles.
Manipulated terminals
Stationary receptacles

## Slide 4: Deformable linear objects
Surgical sutures
Ropes
[Moll et al. 2006]
[Saha et al. 2007]
Wire harnesses
[Jiang et al. 2010]
DLO networks (DLONs)
[Yan et al. 2020]
[Zhou et al. 2020]
Deformable linear objects (DLOs)
Strings

## Slide 5
Most DLO research focuses on dual arm manipulation with shape perception for shape goals
But practical harness installation scenarios involve confined environments
limited visibility, and are specified by
endpoint goals
 | No. manipulators | Measurement | Goal | DLO networks
Multi-arm, marker-based harness installation [Jiang et al. 2010] | ≥ 2 | keypoints | keypoints | yes
Vision-based DLO shape control w/ learned predictive model [Yan et al. 2020] | 1 | shape | shape | no
Dual-arm shape control w/ adaptive model [Yu et al. 2021] | 2 | shape | keypoints | no
Dual-arm shape control with learned graph network model [Wang et al. 2022] | 2 | shape | shape | no
Dual-arm shape control with explicit DLO model [Lv et al. 2022] | 2 | shape | shape | no
DLO endpoint casting w/ endpoint measurements [Lim et al. 2022] | 1 | endpoint | endpoint | no
DLON endpoint feedback control w/ endpoint measurements [Ours] | 1 | endpoints | endpoints | yes
Notes: The majority of DLO manipulation research focuses on dual arm manipulation with perception of the full DLO shape, or state.
In practical scenarios, like automotive wire harness installation, confined environments and limited visibility complicate these assumptions.
Confined environments are better suited to single manipulators
And limited visibility may lead to spatially sparse measurements.

## Slide 6
We investigate single-arm installation
of planar DLO networks
with terminal pose measurements and goals
DLON shape, or state , is not known
Terminal poses, or outputs , are continuously measured
Held terminal velocity is the input
Static receptacle poses are goals
Installation requires sequence of terminal manipulations (TMs):
Manipulate
Pose:
Output:
Free terminals subject to
Release terminal
If successful insertion (:
Grasp terminal

## Slide 7
Installation requires sequence of terminal manipulations (TMs):
Manipulate
Free terminals subject to
Release terminal
If successful insertion (:
Grasp terminal
unknown and time-varying
free terminals should remain graspable
Remain within reachable workspace
Maintain gripper clearance from obstacles
TM Sequence Planner
DLON
Terminal pose goals
TM Controller
Vision system
Grasp terminal
Terminal manipulation
Adaptive model
Constrained MPC

## Slide 8
Adaptive model
Do direct input-output dynamics exist? :
What is the structure of ?
Can be approximated online?
Empirical observation: Given fixed terminal poses , the DLON returns to a stable shape
Hypothesis: the output map is approximately invertible:
such that
If so, then:
✓
reconstruction error
Notes: Methodology:
Excite simulated DLON and collect dataset
Fit models and draw insights
Develop general DLON model

## Slide 9
Dataset
Simulated DLON
Random excitations
Neural network approximations of
Supervised learning
Training error indicates good fit
reconstructs
Approximate inversion hypothesis supported
How can be approximated in an interpretable way?
NN approximation of
Notes: Methodology:
Excite simulated DLON and collect dataset
Fit models and draw insights
Develop general DLON model

## Slide 10: Sparse Identification of Nonlinear Dynamics (SINDy)
Objective: Learn from dataset using a library of nonlinear terms:
Then solve for sparse coefficients using regularization
[Brunton et al. 2016]
Polynomial model predicts dynamics, though rougher than NN model

## Slide 11: Polynomial model admits useful decomposition
  We find significant rigid body dynamics in
  Where, for free terminal subject to held terminal velocities :
RB dynamics explanation frequency over all samples in

## Slide 12: Adaptive ensemble model
Local linear model:
where is approximated over the last samples:
Learns subtle relationships between free terminals
Estimation involves delay and control excitation
Global rigid body model:
where is known and fixed
Can be deployed immediately without delay
Captures only bulk dynamics
Ensemble model that captures benefits of both:
where is trust in rigid body model and decays over time at rate
Maximum prediction errors over 5 seconds using last 1 second of data:

## Slide 13: Terminal manipulation controller and sequence planner
Controller drives held terminal to goal without driving free terminals into constraint violation:
Planner heuristically chooses the next terminal to hold based on current constraint proximity:

## Slide 14: Simulation experiments
Applied framework with rigid body model and ensemble model to increasingly challenging problems

## Slide 15
Ensemble model
(a) easy
(b) rotated
The framework performs well on simple problems with either the ensemble model or rigid body model alone.
Playback speed: 4x
Notes: Our framework performs well on simple problems with either the ensemble model or rigid body model alone. Here, each terminal is to be connected to a receptacle of the same color.

## Slide 16
(c) obstacle
When navigating through a narrow opening, the framework with the ensemble model succeeds, while that with the rigid body model becomes stuck.
Does not finish
Rigid body model
Ensemble model
Playback speed: 4x
Notes: For more complex problems, like navigating through a narrow opening, the framework using the ensemble model succeeds while the rigid body model fails, indicating that the local regression model learns important components of the dynamics

## Slide 17
(d) hall
When navigating around a wall of obstacles, the framework with both models succeed, but that with the ensemble model avoids obstacles more reliably.
Rigid body model
Ensemble model
Playback speed: 8x
Notes: In other challenging problems, both models succeed, but the framework with the ensemble model avoids obstacles more reliably.

## Slide 18
Magnetic mating to simulate insertion
Modified automotive wire harness
Static receptacles
Physical case study: automotive wire harness installation
Framework with ensemble model solves problem with a variety of initial conditions without a priori learning or system identification.
Playback speed: 10x
(b) basic
(c) bunched
(d) tough
Notes: To evaluate the generality of the framework, we consider a physical case study of automotive wire harness installation
A modified wire harness with 3 terminals [ ] is to be mated to to three static receptacles.
The framework with the ensemble model solves installation problems with a variety of initial conditions without a priori knowledge of dynamics or system identification

## Slide 19
initially ungraspable due to obstacle proximity
planner chooses to hold T1 and use it to pull T2 out of constraint violation
t2
t1
t2
t1
t2
t0
Sequence planner reasons about present grasp feasibility.
Notes: The sequence planner reasons about the present grasp feasibility.
In this case, T2 is initially ungraspable due to obstacle proximity.
So the planner chooses to hold T1 and use it to pull T2 out of constraint violation

## Slide 20
Once held, the MPC selects using the ensemble model to predict
Sequence planner reasons about present grasp feasibility.
Controller preserves future grasp feasibility.
Notes: The controller preserves future grasp feasibility.
Once held, the MPC selects u using the ensemble model to predict the velocity of T2

## Slide 21
Sequence planner reasons about present grasp feasibility.
Controller preserves future grasp feasibility.
Notes: to ensure it does not enter an infeasible region during manipulation.

## Slide 22: Conclusions
Planar DLON output maps are approximately invertible:
such that
Direct output dynamics exist
:
and can be decomposed into rigid body and residual terms, leading to an adaptive ensemble model that generalizes to new DLONs:
Based on the above, our planning and control framework can solve a variety of DLON installation problems without offline training or online excitation.

## Slide 23: Future work
Validation on more complex DLONs
Leverage output map invertibility to predict state and satisfy state constraints
Utilize data collected from iterative installations to build global model and enable more intelligent planning.
[Wang et al. 2022]

## Slide 24
Terminal sequence planner
DLON
Terminal pose goals
Held terminal controller
Vision system
Grasp terminal
Move held terminal
Adaptive model
Constrained MPC
Input-output model without state dependence:
Rigid body model
Local regression model
Composite model
Notes: In this work, we investigate single-arm manipulation [ ] of planar DLO networks [ ] with terminals pose measurements
This means that the overall shape of the DLON, or its state, is not known
Instead, the terminal poses, or outputs, are continuously measured
The manipulator holds a single terminal at a time and the commanded velocity of the held terminal is the input to the system
The goal poses of all terminals are given, and a planner selects which terminal to grasp next.
The held terminal controller generates velocity command inputs to the DLON system
A vision system provides continuous terminal pose measurements to the controller and planner.
The held terminal controller consists of a model predictive controller with task-relevant constraints, [ ] which uses an adaptive model learned online
The adaptive model predicts output dynamics without knowledge of the state or state dynamics
We approximate output dynamics with an composite model, [ ] which is composed of a general rigid body model, which enables control without prior learning, and a local regression model that gradually incorporates learned dynamics.

## Slide 25
We investigate single-arm installation
of planar DLO networks
with terminal pose measurements and goals
DLON shape, or state , is not known
Terminal poses, or outputs , are continuously measured
Held terminal velocity is the input
Static receptacle poses are goals
Installation requires sequence of terminal manipulations (TMs):
Manipulate
Pose:
Output:
Free terminals subject to
Release terminal
If successful insertion (:
Grasp terminal